## Slide 1: Natural Gas Storage Assets Optimization
by
Saurabh Chalke
B00791586
Master of Engineering
Department of Industrial Engineering
07, November 2019

## Slide 2: Content:
Overview of Natural Gas (NG) industry
Problem Statement
Key Assumptions
Modeling approach
Linear Programming
Stochastic Linear Programming
Min-Max Regret
Robust Optimization
Deterministic Dynamic Programming
Model Summary
NG storage Graphic User Interface tool
References
07, November 2019

## Slide 3: Overview of Natural Gas (NG) Industry:
NG offers a clean and efficient fuel burning method.
Canada is the fourth largest NG producer in the world and as per Canadian Gas Association report dated January’2018, NG meets over 30% of Canada’s energy demand.
The demand for NG across North America varies throughout the year and so its prices.
NG storage assets plays a vital role across all the supply chain elements.
NG storage contracts are evaluated mostly based on the past records and experiences.
07, November 2019

## Slide 4
Problem
Statement:
Develop an optimization framework for natural gas storage asset operation using several Linear Programming and Dynamic Programming modeling approaches considering the uncertainty of NG prices.
The primary objective of the project is to maximize the expected profit based on the forecasted price data.
Source: https://www.ingaa.org/File.aspx?id=27274&v=3c5b7072
07, November 2019

## Slide 5
Injection and withdrawal of NG can not occur in the same time period.
NG Asset is available for 24 months.
NG Storage asset returns to its initial state at the end of last time period.
Inventory holding cost is ignored.
Loss of NG during injection/withdrawal and evaporation losses are ignored.
07, November 2019
Key Assumptions:

## Slide 6: Modeling Approach:
Linear Programming -Average Monthly Price (LP)
Stochastic Linear Programming -K Price Simulations (SLP)
Stochastic Linear Programming with Chance Constraint
Minimizing the Maximum Regret (MMR)
Robust Optimization (RO)
Deterministic Dynamic Programming (DDP)
07, November 2019

## Slide 7: Linear Programming (Average Monthly Price)
07, November 2019
Sets:
Variables:
Parameters:

## Slide 8: Linear Programming (Average Monthly Price) (Cont’d)
Operating Characteristics:
 | 0
 | 0
 | 24 months
Price Simulations | 962
 | 0
 | 0
 | 24 months
Price Simulations | 962
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -220000 | 305000 | 305000 | 0 | 0 | -85000 | -457500 | -457500 | 0 | 305000 | 305000 | 305000 | -152500 | -457500 | 305000 | 305000 | -457500 | -457500
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 390000 | 695000 | 1000000 | 1000000 | 1000000 | 915000 | 457500 | 0 | 0 | 305000 | 610000 | 915000 | 762500 | 305000 | 610000 | 915000 | 457500
Expected Profit: $ 534,555/-
Computational Time: 1.875 sec.
07, November 2019

## Slide 9: Model Summary
07, November 2019

## Slide 10: Modeling Approach:
Linear Programming -Average Monthly Price (LP)
Stochastic Linear Programming -K Price Simulations (SLP)
Stochastic Linear Programming with Chance Constraint
Minimizing the Maximum Regret (MMR)
Robust Optimization (RO)
Deterministic Dynamic Programming (DDP)
07, November 2019

## Slide 11
Converting the price scenarios into definite number of price vectors (scenarios) using K-Means Clustering Algorithm
Steps:
Initial cluster assignment: Randomly assign a number, from 1 to K, to each of the observations.
Calculate the mean for all the clusters (mean of cluster K is the vector of p features).
Re-assign the observations to the nearest mean.
Iterate the step 2 and 3 until the cluster assignments stop changing.
07, November 2019
Stochastic Linear Programming (K Price Simulations)

## Slide 12
07, November 2019
A good clustering is one for which the within-cluster variation is as small as possible.
Stochastic Linear Programming (K Price Simulations) (Cont’d)

## Slide 13
Deriving the Optimum number of price scenarios using “Elbow Method”
07, November 2019
Chart: Optimal #Price Scenarios
Total Withinness | 332.385 | 267.8576 | 247.28 | 232.7457 | 223.083 | 217.5915 | 204.52 | 203.6617 | 194.1582 | 193.7671 | 187.8496 | 186.0449 | 183.5504 | 177.6937 | 175.8295
Stochastic Linear Programming (K Price Simulations)
(Cont’d)
Chart: K=9 price vectors over a time horizon of 24 months.
| 43466 | 43497 | 43525 | 43556 | 43586 | 43617 | 43647 | 43678 | 43709 | 43739 | 43770 | 43800 | 43831 | 43862 | 43891 | 43922 | 43952 | 43983 | 44013 | 44044 | 44075 | 44105 | 44136 | 44166
C1 | 4.0943 | 3.902 | 3.5271 | 2.7982 | 2.6741 | 2.6922 | 2.7218 | 2.7242 | 2.7043 | 2.7372 | 2.7809 | 2.9527 | 3.0816 | 3.0244 | 2.8152 | 2.4465 | 2.4044 | 2.4706 | 2.5349 | 2.5368 | 2.5135 | 2.5257 | 2.5816 | 2.7669
C2 | 4.7362 | 4.5671 | 4.2407 | 2.9351 | 2.7821 | 2.7964 | 2.8191 | 2.8152 | 2.7963 | 2.8203 | 2.8799 | 3.026 | 3.1398 | 3.079 | 2.8814 | 2.4911 | 2.4484 | 2.5062 | 2.5573 | 2.5616 | 2.5504 | 2.5631 | 2.6496 | 2.8126
C3 | 4.6979 | 4.5297 | 4.1985 | 2.9109 | 2.762 | 2.776 | 2.8004 | 2.7973 | 2.7739 | 2.8003 | 2.8406 | 2.9945 | 3.1171 | 3.0575 | 2.8524 | 2.4709 | 2.4261 | 2.484 | 2.5429 | 2.5458 | 2.5258 | 2.5395 | 2.6141 | 2.7898
C4 | 5.0659 | 4.8917 | 4.6402 | 2.962 | 2.7641 | 2.7774 | 2.797 | 2.7903 | 2.7651 | 2.7896 | 2.8314 | 2.9981 | 3.1176 | 3.0635 | 2.8668 | 2.4574 | 2.4115 | 2.4721 | 2.534 | 2.5377 | 2.5177 | 2.5323 | 2.6115 | 2.7864
C5 | 4.659 | 4.4944 | 4.1703 | 2.9104 | 2.7629 | 2.7782 | 2.8017 | 2.7995 | 2.7785 | 2.8043 | 2.835 | 2.991 | 3.1154 | 3.0576 | 2.8507 | 2.4852 | 2.4419 | 2.4999 | 2.558 | 2.5612 | 2.5425 | 2.5562 | 2.6185 | 2.7925
C6 | 4.6457 | 4.4815 | 4.1558 | 2.8986 | 2.75 | 2.7649 | 2.7895 | 2.7865 | 2.765 | 2.7912 | 2.8265 | 2.9837 | 3.1076 | 3.0496 | 2.8449 | 2.474 | 2.429 | 2.487 | 2.5458 | 2.5488 | 2.5292 | 2.5432 | 2.6104 | 2.7852
C7 | 4.6006 | 4.4402 | 4.1133 | 2.8745 | 2.7278 | 2.7429 | 2.7688 | 2.7658 | 2.7439 | 2.7708 | 2.799 | 2.964 | 3.0921 | 3.0351 | 2.8247 | 2.4616 | 2.4176 | 2.4756 | 2.5348 | 2.5378 | 2.5175 | 2.5317 | 2.5912 | 2.7728
C8 | 4.591 | 4.4304 | 4.0991 | 2.8484 | 2.7029 | 2.7178 | 2.745 | 2.7415 | 2.7154 | 2.7448 | 2.7913 | 2.9527 | 3.08 | 3.023 | 2.814 | 2.4387 | 2.3938 | 2.4524 | 2.5135 | 2.516 | 2.4934 | 2.5081 | 2.5815 | 2.7618
C9 | 4.6437 | 4.4796 | 4.1511 | 2.886 | 2.7367 | 2.7518 | 2.7766 | 2.7737 | 2.752 | 2.7776 | 2.8178 | 2.9763 | 3.1006 | 3.0426 | 2.8368 | 2.462 | 2.4175 | 2.4755 | 2.535 | 2.5378 | 2.5171 | 2.5312 | 2.6025 | 2.7782

## Slide 14
07, November 2019
Stochastic Linear Programming (K Price Simulations)
(Cont’d)
Calculating the Cluster (Scenario) Probability :
 | C1 | C2 | C3 | C4 | C5 | C6 | C7 | C8 | C9
Cluster size: | 2 | 37 | 89 | 8 | 143 | 294 | 110 | 41 | 238
Total #Observations: | 962 | 962 | 962 | 962 | 962 | 962 | 962 | 962 | 962
Cluster Probability: | 0.002 | 0.038 | 0.093 | 0.008 | 0.149 | 0.306 | 0.114 | 0.043 | 0.247

## Slide 15: Stochastic Linear Programming (K Price Simulations) (Cont’d)
07, November 2019
Sets:
s
Variables:
Parameters:

## Slide 16
Stochastic Linear Programming -K Price Simulations (SLP) (Cont’d)
Operating Characteristics:
 | 0
 | 0
 | 24 months
Price Simulations | 9
 | 0
 | 0
 | 24 months
Price Simulations | 9
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -252978.1705 | 303347.1933 | 305000 | 34630.9771 | 0 | -85000 | -457500 | -457500 | 0 | 305000 | 305000 | 305000 | -143365.3846 | -451634.6154 | 305000 | 290000 | -457500 | -457500
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 357021.8295 | 660369.0229 | 965369.0229 | 1000000 | 1000000 | 915000 | 457500 | 0 | 0 | 305000 | 610000 | 915000 | 771634.6154 | 320000 | 625000 | 915000 | 457500
Expected Profit: $ 534,638/-
Computational Time: 2.33 sec.
07, November 2019

## Slide 17: Model Summary
07, November 2019

## Slide 18: Modeling Approach:
Linear Programming -Average Monthly Price (LP)
Stochastic Linear Programming -K Price Simulations (SLP)
Stochastic Linear Programming with Chance Constraint
Minimizing the Maximum Regret (MMR)
Robust Optimization (RO)
Deterministic Dynamic Programming (DDP)
07, November 2019

## Slide 19: Stochastic Linear Programming with Chance Constraint
Where,
Equivalent LP form:
--------(1)
---------(2)
07, November 2019
Adding constraint eq. (1) & (2) and binary variable in the SLP formulation.
values are varied from $520,000 to $554,000 in a step size of $100
(520000, 520100,…,554000)
values are varied from 0 to 1 in a step size of 0.05
(0, 0.05, 0.10,…,1.00)

## Slide 20: Stochastic Linear Programming with Chance Constraint (Cont’d)
07, November 2019
Chart: Confidence Level vs. Desired Profit
Expected Profit as per SLP = $ 534,638/-
Computational Time: 6.95 minutes

## Slide 21: Modeling Approach:
Linear Programming -Average Monthly Price (LP)
Stochastic Linear Programming -K Price Simulations (SLP)
Stochastic Linear Programming with Chance Constraint
Minimizing the Maximum Regret (MMR)
Robust Optimization (RO)
Deterministic Dynamic Programming (DDP)
07, November 2019

## Slide 22: Minimizing the Maximum Regret (MMR)
Steps:
Solving the LP for K-price scenarios individually to get the vector data as an input to the Min-Max Regret model.
Solving Min-Max Regret model using vectors as parameters
07, November 2019

## Slide 23
Steps:
Solving the LP for K-price scenarios individually to get the vector data as an input to the Min-Max Regret model.
Solving Min-Max Regret model using vectors as parameters
07, November 2019
Minimizing the Maximum Regret (MMR) (Cont’d)

## Slide 24
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -220000 | 305000 | 305000 | -305000 | 305000 | -85000 | -457500 | -457500 | 0 | 305000 | 305000 | 305000 | 85000 | -72369.385 | 72369.385 | -340952.92 | -201547.08 | -457500
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 390000 | 695000 | 1000000 | 695000 | 1000000 | 915000 | 457500 | 0 | 0 | 305000 | 610000 | 915000 | 1000000 | 927630.615 | 1000000 | 659047.08 | 457500
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -244447.92 | 305000 | 305000 | 24447.918 | 0 | -85000 | -457500 | -457500 | 0 | 305000 | 305000 | 305000 | -151746.06 | -457500 | 305000 | 304246.06 | -457500 | -457500
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 365552.08 | 670552.08 | 975552.08 | 999999.998 | 999999.998 | 914999.998 | 457499.998 | -0.002 | -0.002 | 304999.998 | 609999.998 | 914999.998 | 763253.938 | 305753.938 | 610753.938 | 914999.998 | 457499.998
LP (962 Scenarios)
Expected Profit: $ 499,684/-
Computational Time: 546.50 sec.
Expected Profit: $ 534,517/-
Computational Time: 2.47 sec.
07, November 2019
Minimizing the Maximum Regret (MMR) (Cont’d)
SLP (9 Scenarios)

## Slide 25: Model Summary
07, November 2019

## Slide 26: Modeling Approach:
Linear Programming -Average Monthly Price (LP)
Stochastic Linear Programming -K Price Simulations (SLP)
Stochastic Linear Programming with Chance Constraint
Minimizing the Maximum Regret (MMR)
Robust Optimization (RO)
Deterministic Dynamic Programming (DDP)
07, November 2019

## Slide 27: Robust Optimization (RO)
O.F. Can be reformulated as:
07, November 2019
Sets:
s
Variables:
Parameters:

## Slide 28
Robust Optimization (RO) (Cont’d)
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -220000 | 305000 | 305000 | -234747.66 | 234747.66 | -85000 | -457500 | -457500 | 0 | 305000 | 305000 | 305000 | 85000 | -367723.01 | 305000 | -22276.987 | -457500 | -457500
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 390000 | 695000 | 1000000 | 765252.34 | 1000000 | 915000 | 457500 | 0 | 0 | 305000 | 610000 | 915000 | 1000000 | 632276.99 | 937276.99 | 915000.003 | 457500.003
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -220000 | 305000 | 305000 | 0 | 0 | -85000 | -457500 | -457500 | 0 | 305000 | 305000 | 305000 | -152500 | -457500 | 305000 | 305000 | -457500 | -457500
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 390000 | 695000 | 1000000 | 1000000 | 1000000 | 915000 | 457500 | 0 | 0 | 305000 | 610000 | 915000 | 762500 | 305000 | 610000 | 915000 | 457500
Expected Profit: $ 430,790/-
Computational Time: 2.87 sec.
Expected Profit: $ 520,449/-
Computational Time: 2.14 sec.
07, November 2019
LP (962 Scenarios)
SLP (9 Scenarios)

## Slide 29: Model Summary
07, November 2019

## Slide 30: Model Summary
07, November 2019

## Slide 31: Modeling Approach:
Linear Programming -Average Monthly Price (LP)
Stochastic Linear Programming -K Price Simulations (SLP)
Stochastic Linear Programming with Chance Constraint
Minimizing the Maximum Regret (MMR)
Robust Optimization (RO)
Deterministic Dynamic Programming (DDP)
07, November 2019

## Slide 32: “Given the current state, an optimal policy for the remaining stages is independent of the policy decisions adopted in previous stages. Therefore, the optimal immediate decision depends on only the current state and not on how you got there. This is the principle of optimality for dynamic programming”.
Deterministic Dynamic Programming (DDP) (Cont’d)
Calculate the expected profit
Optimal decisions for all stages
Perform backward recursion
Discreet States, Stages, and Policy variables
07, November 2019
Steps:

## Slide 33
Deterministic Dynamic Programming (DDP) (Cont’d)
07, November 2019
Backward Recursion
Optimal Decisions

## Slide 34
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -252978.1705 | 303347.1933 | 305000 | 34630.9771 | 0 | -85000 | -457500 | -457500 | 0 | 305000 | 305000 | 305000 | -143365.3846 | -451634.6154 | 305000 | 290000 | -457500 | -457500
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 357021.8295 | 660369.0229 | 965369.0229 | 1000000 | 1000000 | 915000 | 457500 | 0 | 0 | 305000 | 610000 | 915000 | 771634.6154 | 320000 | 625000 | 915000 | 457500
32
Deterministic Dynamic Programming (DDP) (Cont’d)
Operating Characteristics:
 | 0
 | 0
 | 0
 | 0
Expected Profit: $ 555,809/-
Computational Time: 18553.9 sec. ~ 5hrs.
07, November 2019
Chart: NG storage asset operation profile
| 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20 | 21 | 22 | 23 | 24
Injection Qty. | 0 | 0 | 0 | 0 | 305000 | 305000 | -220000 | 305000 | 305000 | 0 | 0 | 0 | -500000 | -500000 | 0 | 305000 | 305000 | 305000 | -25000 | -500000 | 305000 | 305000 | -500000 | -500000
Inventory in hand | 0 | 0 | 0 | 0 | 0 | 305000 | 610000 | 390000 | 695000 | 1000000 | 1000000 | 1000000 | 1000000 | 500000 | 0 | 0 | 305000 | 610000 | 915000 | 890000 | 390000 | 695000 | 1000000 | 500000

## Slide 35
Model Summary
07, November 2019

## Slide 36: NG Storage Asset User Interface Tool
Click Here
07, November 2019

## Slide 37: References:
Mausser H. and Laguna M. A New Mixed Integer Formulation for the Maximum Regret Problem. International Transactions in Operational Research Vol. 5, No. 5, pp. 389-403,1998
Avery W., Brown G. G., Rosenkranz J. A. & Wood R. K. (1992). Optimization of Purchase, Storage and Transmission Contracts for Natural Gas Utilities. Operations Research, 40(3), 446-462. doi:10.1287/ opre.40.3.446
F. Hillier & G. Lieberman. Introduction to Operations Research-Chapter 7 & 11.
Nandalal K. & Bogardi J. Dynamic programming-based operation of reservoirs. Cambridge University Press
G. James, D. Witten, T. Hastie & R. Tibshirani. An Introduction to Statistical Learning. Chapter 10.
https://www.nrcan.gc.ca/science-data/data-analysis/energy-data-analysis/energy-facts/natural-gas-facts/20067
07, November 2019

## Slide 38
07, November 2019